## Slide 1
PROTOTYPE TECHNOLOGY DEMONSTRATOR
XRIM-117 WYVERN
Autonomous Guided Demonstrator Platform
70mm · Active mid fins + passive aft stabilizers · Ceramic jetavane TVC · 3-board distributed avionics · 915MHz datalink
Skylight Industries LLC · PDR-002 Rev A · CONFIDENTIAL

## Slide 2
MISSION
Why WYVERN?
A hardware-first approach to validating guided autonomous flight control in a subscale, recoverable, repeatably-flyable platform.
70mm
OD
body diameter
10
srvs
total actuators
915
MHz
datalink range
3
PCBs
avionics stack
OBJECTIVES
Programme Objectives
Validate hybrid control architecture
Demonstrate coordinated aerodynamic fin + ceramic jetavane TVC authority across boost, loiter, and landing burn phases.
Prove distributed avionics concept
Three-board redundant-sensor architecture with independent power domains and fault detection.
Demonstrate powered vertical recovery
Full-profile autonomous flight: rail launch → guided ascent → altitude loiter → propulsive landing.
Generate quantitative flight data
Log 100Hz sensor fusion data via 915MHz LoRa for post-flight control law validation.

## Slide 3
VEHICLE
Vehicle Configuration
Chute bay
ASAM-1 · mid fins
CCM · avionics · LoRa
ASAM-2 · jetavane · sustainer
Booster · eject ring
SCALE
1:2.14 of full system
DIAMETER
70mm OD
LENGTH
~1,170mm
MASS (EST.)
~640g all-up
STRUCTURE
PETG-CF printed
FIN RINGS
1× active + 1× passive
TVC
Ceramic jetavane
PROPULSION
2-stage solid motor
RECOVERY
Computer-triggered chute
DATALINK
915MHz LoRa · ~2km LoS

## Slide 4
CONTROL
Hybrid Control Architecture
WYVERN employs a cascaded PID control system that blends aerodynamic authority from an active mid fin ring (Ring 2) with thrust-vector control from ceramic jetavanes. Passive aft fins (Ring 1) provide baseline stability. Authority allocation shifts with dynamic pressure.
Outer loop — altitude
PID on altitude error → pitch/yaw setpoint
Inner loop — attitude
PID on quaternion error → fin + jetavane commands
TVC mixing
Pitch: jetavane A · Yaw: jetavane B · decoupled
Fin mixing
Pitch ±: top/bottom · Yaw ±: left/right · Roll: Ring 2 collective cant (45° clocking)
Control authority by phase
Boost
85%
Rail clear
60%
Loiter
30%
Descent
50%
Landing burn
80%
Jetavane TVC
Aerodynamic fins

## Slide 5
AVIONICS
3-Board Distributed Avionics Stack
ASAM-1
Mid Ring Controller
STM32F411 · Cortex-M4 100MHz
ICM-42688-P IMU · MS5611 baro
4× servo PWM · 7.4V HV rail
1S 1000mAh independent LiPo
CCM
Central Command Module
RP2040 · dual-core 133MHz
Primary IMU + barometer
3× pyrotechnic MOSFET channels
LoRa 915MHz · ~2km datalink
ASAM-2
TVC + Sustainer Controller
STM32F411 · Cortex-M4 100MHz
ICM-42688-P IMU · MS5611 baro
3× servo PWM (jetavane + slide)
Sustainer ignition relay
All boards: 62mm circular · 2-layer FR4 · ENIG · EasyEDA design · JLCPCB fabrication + SMT assembly · Power fully independent per board · JST-GH 8-pin inter-board ribbon

## Slide 6
FLIGHT PROFILE
Autonomous 8-Phase Flight Profile
0
Safe
Pre-arm · servos neutral
1
Armed
IMU cal · GCS link · pyro continuity
2
Boost
Booster ignites · rail exit
3
Rail clear
Fins active · attitude hold
4
Staging
Booster eject · sustainer ignition
5
Loiter
Altitude hold · jetavane + fins
6
Descent
Thrust-modulated landing burn
7
Touchdown
Impact detect · disarm
Phase 8 — ABORT
GCS abort command OR attitude error >45° for >0.5s OR altitude runaway → ejection charge fires → nose cone separates → 24in parachute deploys → ballistic recovery
~120m
target altitude (nominal)
10–20s
loiter duration
<1 m/s
touchdown velocity
100Hz
sensor log rate

## Slide 7
TVC
Ceramic
Jetavane TVC
Two Macor ceramic vanes sit in the nozzle exhaust stream on titanium shafts. Each vane rotates ±45° to simultaneously deflect the thrust vector and partially occlude the nozzle exit — providing both attitude control and analogue thrust modulation from a single actuator per axis.
Vane material
Macor / ZTA ceramic
Vane rotation
±45° per axis
Thrust range
~35–100% of rated
Actuator
KST X08 Plus HV
Axes
Pitch + Yaw independent
Fail-safe
Spring return → full thrust
HOW IT WORKS
How jetavane TVC works
1
Vane at 0° — full thrust, neutral vector
Vane aligned with flow. Minimal blockage. Motor delivers rated thrust. No deflection.
2
Vane rotated — vectored exhaust
Rotation deflects exhaust stream up to ~20° from motor axis. Generates corrective torque on vehicle without moving the motor.
3
Vane near 90° — thrust reduction
Vane near-perpendicular to flow. Exit area partially blocked. Effective thrust reduced to ~35% for landing burn deceleration.
Historical precedent: V-2 rocket (1942) and early surface-to-air systems used graphite jetavanes on identical principles. WYVERN applies this to a hobby-scale platform with ceramic materials and closed-loop digital control.

## Slide 8
PROGRAMME
Build & Test Programme
Phase 1
Design & Fabrication
Wks 1–3
OpenRocket model + stability verification
PETG-CF parts CAD (nose, fin cans, TVC frame)
PCB design in EasyEDA — 62mm circular
Phase 2
Print & Mechanical
Wks 3–5
Print all PETG-CF structural parts
Jetavane shaft + ceramic vane assembly
Booster ejection ring + spring test
Phase 3
Electronics
Wks 5–7
Receive JLCPCB SMT boards
Firmware flash + IMU/baro calibration
Full 6-servo bench sweep test
Phase 4
Integration & Ground Test
Wks 7–8
Ejection charge ground test
Jetavane static fire test
Full GCS datalink verification
Phase 5
Flight Test Campaign
Wk 9+
Flight 1: booster only · recovery verify
Flight 2: two-stage · no landing burn
Flight 3+: full profile · progressive altitude

## Slide 9
BUDGET
Programme Budget Overview
~$660
estimated build cost — single vehicle
$145
One-time PCB setup
Subsequent builds ~$280 total
2
Flights per motor set
$124 recurring cost
wks
Months to first flight
5-phase structured programme
All components sourced from commercial hobby and COTS electronics suppliers. No custom tooling required.

## Slide 10
XRIM-117 WYVERN
Let's talk.
Skylight Industries LLC · PDR-002 Rev A
XRIM-117 WYVERN Prototype Technology Demonstrator
Autonomous guided demonstrator platform · 70mm · active mid fins + passive aft stabilizers · ceramic jetavane TVC · 3-board distributed avionics
CONFIDENTIAL · FOR DISCUSSION PURPOSES ONLY · NOT FOR DISTRIBUTION